EMUBT BOARD INSTALLATION MANUAL

1	This is your Digifant ECU, I tested at least three versions: DM, CP and B (purple one)

2	After opening the ECU you should see white plastic sheet and under it metal cover. If there is no metal cover you are not the first one who opens it :D

3	There should be screws on top of metal cover and on PCB as well, unscrew all of them and open it like below

4	Remove the metal cover, there should be Motorola microntroller and EEPROM chip

5	Remove the chip carefully with some flat small knife

6	Locate C68 capacitor on the board, you need to connect RX0 pad of EMUBT board with it like on the picture

7	Install the board in EEPROM socket, it will fit only in one position, check the picture below

8	Close the ECU, everything should fit nice :D